## Slide 1: How We See the Invisible World – Microbiology Techniques
Chapter 2
Biology 2161

## Slide 2: The Invisible World

## Slide 3: Properties of Light
The amplitude is the height of a wave, whereas the wavelength is the distance between one peak and the next.
These waves have different frequencies, or rates of vibration. The wave at the top has the lowest frequency, since it has the fewest peaks per unit time. The wave at the bottom has the highest frequency.

## Slide 4: Lens and Refraction

## Slide 5: Reflection and Refraction
Reflection: Waves bounce off a material
Refraction: Light waves change direction as they enter a new medium
  Change speeds depending on the medium
  How much the speed slows depends on the medium – refractive index
  Light moves slower through water than air. Light entering water from air changes direction greatly

## Slide 6: Convex and Concave Lens

## Slide 7: Visible Light Spectrum

## Slide 8: Magnification and Resolution
Two key characteristics of microscopes: magnification and resolving power
Magnification
  Results when visible light waves pass through a curved lens
    The light experiences refraction (bent)
Light rays are beamed to a ‘focal point’ . Travel through the focal point and spread apart forming an ‘enlarged image.

## Slide 9
Figure 3.13

## Slide 10: Principles of Light Microscopy
Magnification- occurs in two phases
  Objective lens
  Ocular lens
Total power of magnification- the product of the power of the objective and the power of the ocular

## Slide 11: Resolution
Resolution- the ability to distinguish two points from one another
Also known as resolving power
  Resolving power (RP) = 0.2 microns
    1 micron = 0.001 mm
Oil immersion lenses increase the numerical aperture of the lens
  NA = ability of a lens to gather light and resolve fine detail in an object being observed.

## Slide 12: Oil Immersion

## Slide 13: Magnification and Resolution
Increased magnification decreases the resolution

## Slide 14: Historical Perspective: Development of the Microscope
Antonie van Leeuwenhoek (1632–1723) is credited as being the first person to observe microbes, including bacteria, which he called “animalcules” and “wee little beasties.”
Even though van Leeuwenhoek’s microscopes were simple microscopes (as seen in this replica), they were more powerful and provided better resolution than the compound microscopes of his day.
Though more famous for developing the telescope, Galileo Galilei (1564–1642) was also one of the pioneers of microscopy. (credit b: modification of work by “Wellcome Images”/Wikimedia Commons)

## Slide 15: Robert Hooke

## Slide 16: Brightfield-Compound Microscopes

## Slide 17: Bright-Field Microscopy
Most widely used
Background or field of view is illuminated
Forms its image when light is transmitted through the specimen
The specimen produces an image that is darker than the surrounding illuminated field
Can be used with live, unstained and preserved, stain specimens

## Slide 19: Dark-field Microscopes

## Slide 20: Dark-Field Microscopy
A bright-field microscope can be adapted to a dark-field microscope by adding a stop to the condenser
The stop blocks all light from entering the objective lens except for peripheral light
The specimen produces an image that is brightly illuminated against a dark field

## Slide 21: Phase Contrast
This figure compares a brightfield image (left) with a phase-contrast image (right) of the same unstained simple squamous epithelial cells. The cells are in the center and bottom right of each photograph (the irregular item above the cells is acellular debris). Notice that the unstained cells in the brightfield image are almost invisible against the background, whereas the cells in the phase-contrast image appear to glow against the background, revealing far more detail.

## Slide 22: Phase-Contrast Microscopy
Transforms subtle changes in light waves passing through a specimen into differences in light intensity
Allows differentiation of internal components of live, unstained cells
Useful for viewing intracellular structures such as bacterial spores, granules, and organelles

## Slide 23: Fluorescence Microscopes

## Slide 24: Fluorescence Microscopy
Includes a UV radiation source and a filter that protects the viewer’s eyes
Used with dyes that show fluorescence under UV rays
Forms a colored image against a black field
Used in diagnosing infections caused by specific bacteria, protozoans, and viruses using fluorescent antibodies
Immunofluorescence: antibody-antigen bonding; used to identify disease-causing organisms

## Slide 25: Electron Microscopes

## Slide 26: Electron Microscopy
Originally developed for studying nonbiological materials
Biologists began using it in the early 1930s
Forms an image with a beam of electrons
  Electrons travel in wavelike patterns 1,000 times shorter than visible light waves
  This increases the resolving power tremendously
Magnification can be extremely high (between 5,000X and 1,000,000X for biological specimens)
Allows scientists to view the finest structure of cells

## Slide 27: Comparison to Light Microscopes

## Slide 28: TEM vs. SEM
a. TEM b. SEM

## Slide 29: TEM
Often used to view structures of cells and viruses
Electrons are transmitted through the specimen
The specimen must be very thin (20-100 nm thick) cut with ultramicrotome and stained to increase image contrast
  Specimens dehydrated, embedded in plastic

## Slide 30
Figure 3.22
TEM images

## Slide 31: SEM
Creates a detailed 3-D image of the specimen
Specimens must be coated with a metal
Electrons manipulated by magnetic field
  Do not pass directly through the specimen
  Bounce across the surface

## Slide 32
Figure 3.23

## Slide 35: Methods of Culturing Microorganisms: The Five I’s
Microbiologists use five basic techniques to manipulate, grow, examine, and characterize microorganisms in the laboratory:
  Inoculation
  Incubation
  Isolation
  Inspection
  Identification

## Slide 36: Streak Plate Method
Streak plate method- small droplet of culture or sample spread over surface of the medium with an inoculating loop
  Uses a pattern that thins out the sample and separates the cells
Figure 3.3 a,b

## Slide 37: Staining Microscopic Specimens

## Slide 38: Positive vs. Negative Staining
These Bacillus anthracis cells have absorbed crystal violet, a basic positive stain.
This specimen of Spinoloricus, a microscopic marine organism, has been stained with rose bengal, a positive acidic stain.
These B. megaterium appear to be white because they have not absorbed the negative red stain applied to the slide. (credit a: modification of work by Centers for Disease Control and Prevention; credit b: modification of work by Roberto Danovaro, Antonio Pusceddu, Cristina Gambi, Iben Heiner, Reinhardt Mobjerg Kristensen; credit c: modification of work by Anh-Hue Tu)

## Slide 39: Simple Stains
Require only a single dye
  Examples include malachite green, crystal violet, basic fuchsin, and safranin

## Slide 40: Differential Stains
Use two differently colored dyes, the primary dye and the counterstain
  Distinguishes between cell types
    Examples include Gram Stain and Acid-fast stain

## Slide 41: The Gram Stain – Differential Stain

## Slide 42: Gram Positive Example

## Slide 43: Mixed Stain

## Slide 44: Acid Fast Stain

## Slide 45: Capsule Staining

## Slide 46: Endospore Staining